## Slide 2: Software Defined Networks CYB 301 Introduction
Egena Onu, PhD.
Computer Science Department,
Bingham University.

## Slide 3: Course Content
SDN
  History
  Motivation
  Concept of SDN
SDN Architecture
SDN Application
SDN Planes
  Control Plane
  Data Plane
  Management Plane
SDN Datapath
Control to Data-plane Interface (CDPI)
SDN Interfaces
  Northbound Interface (NBI)
  Southbound Interface (SBI)
Deployment models
Application areas of SDN
Security using SDN paradigm

## Slide 4: Delivery
Total Contact Hour: 45
Exam: 60%
Tests: 30%
Attendance (80%): 10%

## Slide 5: Software Defined Networks (SDN)
Notes: The modern computer network has evolved into a complex beast that is challenging to manage and which struggles to scale to the requirements of some of today’s environments.
SDN represents a new approach to computer networking that attempts to address these weaknesses of the current paradigm.
SDN is a fundamentally novel way to program the switches utilized in modern data networks.

## Slide 6: Introduction to SDN
Computing has greatly evolved in the last two decades.
Former communication networks (for example, 1G/2G/3G mobile networks, industrial networks, enterprise networks) used specialized and thus costly equipment which make it expensive/difficult to make an experiment at a large scale.
In addition, traditionally the data and control plane elements were bounded in one network element (switch/router) and vendor specific.
Notes: Such a closed structure of the system enables the access only to the vendors, to modify the network according to customer requirements.
SDN overcomes all of these hurdles and offers an approach where the control plane and the data plane are separated providing a central control point (called controller) for centrally coordinating and managing a network.

## Slide 7: SDN
A network in which the control plane is physically separate from the data plane.
A single (logically centralized) control plane controls several forwarding devices.

## Slide 8: Concept of SDN
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Control
Control
Control
Control
Control
Global Network Map
Control Plane
Control
Program
Control
Program
Control
Program
Notes: Talk about forwarding & control planes

## Slide 9: Motivations of SDN
The most important motivation for SDN is the operational challenges involved in managing a computer network.
There are two primary operational challenges.
  Time to effect changes.
  Risk of malfunctioning.
Notes: Time to affect changes: The distributed nature of a network makes it difficult and time-consuming to effect changes in settings of all network elements. It increases with the geographical span of the network and directly impacts the cost of operations.
Risk of malfunctioning: This is somewhat related to the first challenge. Because of the time and effort involved in provisioning, it is increasingly cumbersome to retract those changes should there be an issue in the network caused by that. Ultimately, this is the reason for lack of innovation on the part of the network administrator to optimize the network performance.

## Slide 10: Motivations of SDN
The idea behind SDN is straightforward. It shifts the configuration functions of network devices to a central system, instead of configuring each intermediate device individually.
In a computer network, the configuration functions mainly involve the control plane settings for packet routing.
By shifting the control plane of every router to a central controller, it is possible to manage the network devices remotely.

## Slide 11: Benefits of SDN
By implementing SDN, organisations stand to gain these benefits:
  Cost reduction.
  Control over traffic.
  Smarter network.
Notes: Cost reduction:
  Because it keeps traffic flowing smoothly and assists with near-instant problem resolution, the IT department is likely to see cost savings happen in a short time.
  Tailor-made hardware, for example, tends to be a pretty high investment. By barring limitations and allowing costs to be proportional to consumption, SDN tends to generate savings in the long run.
  It also helps to improve the quality of services and/or products offered by the organization to the final consumer.
  Control over traffic:
  Through the SDN management console, administrators can establish rules on how traffic will occur. Thus improving the overall content deliver and ensuring a pleasant browsing experience for users.
  It also allows network behavior to be controlled by software located beyond the devices that provide physical connectivity. The most obvious result is that operators can adjust the behavior of their SDNs to support new services, which also extends to individual customers.
  Therefore, by decoupling software from hardware, it is perfectly feasible to present innovative services with agility, without the restrictions that we usually see in closed platforms.
Smarter networks:
  SDN helps responsible employees or service providers to create solutions to reduce downtime to allow for adequate recovery planning. It is necessary in extreme cases.
  Resource management in SDN can be innovative and more intelligent. In an SDN, devices operate autonomously with limited recognition of the network. Now, control, restoration, security and bandwidth policies are optimizable. This allows service providers to gain a complete overview of the network and choose how to use it according to their needs.

## Slide 12: Questions!!!